Present and future surface emissions of atmospheric compounds

Prepared by

Jos Olivier, Jeroen Peters

Netherlands Environmental Assessment Agency MNP-RIVM

Bilthoven, The Netherlands

Claire Granier, Gabrielle Pétron

IPSL, Paris, France

Jean-François Müller, Sabine Wallens

Belgian Institute for Space Aeronomy, Brussels, Belgium

Citation of this report: Olivier, J., J. Peters, C. Granier, G. Pétron, J.F. Müller, and S. Wallens, Present and future surface emissions of atmospheric compounds, POET Report #2, EU project EVK2-1999-00011, 2003.

For more information, contact:

Jos Olivier: jos.olivier@rivm.nl

Claire Granier: claire.granier@aero.jussieu.fr

Jean-François Müller: jfm@oma.be

Table of Contents:

| 1. Introduction | 4 |
| --- | --- |
| 2. Anthropogenic emissions during the 1990-2000 period | 4 |
| 2.1 Inventory for 1990, 1995 and 1997 | 4 |
| 2.2 Uncertainty in emissions | 6 |
| 2.3 Temporal variation | 8 |
| 2.4 Emission changes over the 1990-2000 period | 9 |
| 2.4.1 Anthropogenic emissions | 9 |
| 2.4.2 Biomass burning emissions over the 1997-2001 period | 11 |
| 2.4.3 Summary | 13 |
| 3. Natural emissions | 13 |
| 4. Future emissions for the period up to 2020 | 16 |
| 5. References | 22 |
| Abstracts presented at international meetings | 23 |
| Publications during the full duration of the project | 25 |

1. Introduction

Surface fluxes of chemical species are difficult to quantify on a global scale. They are difficult to measure directly, due to their large spatial and temporal variability. Over the past few years, high resolution global inventories have been developed within national, European or international projects. The more recent available inventory is characteristic of 1990 statistics. Within the project, emission distributions for the 1990-2000 period have been developed, that have been used in POET models for different activities, the model intercomparison (see the “Intercomparison of chemistry-transport models” report), the inverse modelling (see the “Optimisation of surface emissions by inverse modelling” report), the simulation of changes in the tropospheric composition over the past decade (see the “Variation of the atmospheric composition over the 1990-2000 period” report), the quantification of the global production of ozone (see the “Global ozone production” report).

Scenarios describing future emissions have been developed in the past, more particularly within IPCC, which describe the evolution of surface emissions of tropospheric constituents such as CO2 and CH4. Within POET, scenarios of the evolution of ozone precursors such as NOx, CO and hydrocarbons, which are not included in the IPCC studies, have been developed. These scenarios take into account emission reduction policies which are consistent with European or international agreements.

This report describes the main characteristics of these inventories. The details on the development of the anthropogenic emission inventories for 1990-1995 are given in Olivier and Berdowski (2001) and Olivier et al. (2001). The documentation on the emissions files used in the models will be published in a MPI technical note in preparation, entitled “The POET 1990-2000 emissions database”.

2. Anthropogenic emissions during the 1990-2000 period

2.1 Inventory for 1990, 1995 and 1997

Version 3 of the EDGAR inventory for anthropogenic emissions has been developed at RIVM, which are typical of years 1990 and 1995. The methodology has been described in Olivier et al. (2001). Basically, activity data from international statistics are used, with data gaps filled by interpolation and extrapolation and emission factors for various source categories to calculation the annual emissions on a per country or per region basis. Next, national total emissions are, per source category, distributed on a 1x1 degree grid using appropriate grid maps for these sources. The EDGAR information system enables to extract the data at various aggregation levels. The inventories, for 1990, 1995 and 1997, by world regions have been first developed, and gridded inventories have been completed next, based on previous spatial distributions. The 1997 inventory has been compiled by combining the inventory for 1995 with regional trend data for various sources for 1995-1997 based on either activity data or reporting emission trends. Details on this approach are provided in Peters and Olivier (2003). Compared to the previous version 2 of the EDGAR inventory, the amounts of agricultural waste burning have been revised substantially, based on recent insights, as shown in Figure 1.

Figure 1.  Changes in agricultural waste burning since 1975 for different areas of the world.

Vegetation fires in temperate climate regions are now also added in the inventory. Figure 2 shows the large variability of the vegetation fires in temperate regions.

Figure 2. Trend in vegetation fires in temperate climate regions.

Globally the largest anthropogenic sources of CO are residential biofuel use and road transport (both 25%), savanna burning (20%) and tropical forest fires (10%). For NOx the largest sources are road transport (25%), electric power generation (20%), industrial fossil fuel combustion and international shipping (both 10%), savanna burning (almost 10%), and residential biofuel use and cement production processes (both about 5%). For total non-methane volatile organic carbon emissions (NMVOC) largest emissions were found to be road transport (about 20%), oil production/handling, residential biofuel use and solvent use (each about 15%), whereas savannah burning and temperate vegetation fires contribute another 5% each. However, these sources are not distributed equally over world regions, let alone individual countries. In OECD and Economies-In-Transition (former USSR, etc.) fossil-fuel use and industrial processes tend to dominate, while in other regions biomass burning, both large-scale as well as biofuel use, often is the largest source. Moreover, some of the largest sources tend to be concentrated in urban areas, e.g. road transport, fuel combustion by industry and power generation, others are most found in the rural area, as can be illustrated when looking at the emissions on a 1x1 degree grid. The shares of regions in the global total and those that determine the trend in the 1990s are given in Table 1, where the four world regions are used that were defined for the SRES scenarios of IPCC (see Section 4).

Table 1. Regional anthropogenic emissions in 1995 in EDGAR 3.2 and 1995-1997 trend (in Tg molecular mass; NOx as NO2).

| Species | Emissions in 1995 | Trend 1995-1997 |
| --- | --- | --- |
|  | OECD | EIT | ASIA | ALM | Total | OECD | EIT | ASIA | ALM | Total |
| CO | 226 | 47 | 251 | 329 | 854 | 5% | -12% | 1% | 1% | 1.1% |
| NOx | 46 | 12 | 30 | 27 | 114 | 2% | -6% | 3% | 7% | 2.7% |
| NMVOC | 55 | 18 | 37 | 51 | 161 | 2% | -13% | 3% | 3% | 0.8% |
| CH4 | 70 | 41 | 117 | 73 | 301 | -2% | -8% | 1% | 2% | -0.5% |

Note: Excluding natural sources; trend without tropical forest fires.

Definition of regions/correspondence with EDGAR 3 regions:

OECD:	OECD'90 (USA, CAN, W EUR, JPN, AUS, NZL);

EIT:	Economies-In-Transition (Reform regions or REF) (i.e. former USSR and Eastern Europe);

ASIA: 	South Asia, East Asia, Southeast Asia;

ALM:	Africa, Latin America, Middle East.

The reference year for the model work and intercomparison is 1997. The total emitted for the chemical species for 1997 included in the POET models are given in Table 2. Here, the emissions for biomass burning have been modified according to recent data compiled by Andreae and Merlet (2001) (see Section 2.4.2).

2.2 Uncertainty

It should be stressed that all emissions have an inherent uncertainty, since most are based on models rather than being measured for the largest sources. It was not feasible to go beyond the uncertainty tables compiled for EDGAR 2.0 (Table 3). However, in addition some conclusions on uncertainty could be drawn from the comparison of Version 2.0 with other datasets as part of the validation. The approach of interpreting uncertainty indications in terms of order-of-magnitude estimate of the uncertainty has been applied for methane and proved to be quite useful for application at global levels. The largest uncertainties in anthropogenic emissions are estimated for large-scale biomass burning, which may also vary substantially between years, biofuel use and for natural sources. Moreover, larger uncertainties appear in case of economies or technologies in transition (e.g. EIT, catalytic converter in cars); changes in emissions can be large in those regions, even in a few years. In these cases accurate monitoring of recent trends proves to be difficult.

Table 2. Global total annual emissions for 1997 (first version of EDGAR 3 and natural sources)

| Species | Anthropo-genic activities | Forest burning | Savanna burning | Agriculture waste burning + fuelwood use | Biogenics/ soils/ lightning | Oceans |
| --- | --- | --- | --- | --- | --- | --- |
| NOx (Tg N) | 28.2 | 1.3 | 2.7 | 2.6 | 8 |  |
| CO (Tg CO) | 336.4 | 119.2 | 150.6 | 247.9 | 160 | 20 |
| CH4 (Tg CH4) | 205.2 | 4.9 | 4.5 | 11.0 |  |  |
| NMVOC: |  |  |  |  |  |  |
| C2H6 (Tg C) | 3.1 | 2.3 | 0.7 | 2.5 | 0.8 | 0.8 |
| C3H8 (Tg C) | 4.9 | 0.4 | 0.2 | 1.0 | 1.6 | 1.0 |
| C2H4 (Tg C) | 2.1 | 4.0 | 1.9 | 4.8 | 4.2 | 1.2 |
| C3H6 (Tg C) | 0.9 | 1.3 | 0.6 | 2.3 | 0.9 | 1.3 |
| Isoprene (Tg C) |  |  |  |  | 500 |  |
| Terpenes (Tg C) |  |  |  |  | 126.7 |  |
| Acetone (Tg C) | 0.6 | 1.0 | 1.1 | 0.1 | 15.0 |  |
| CH2O (Tg C) | 0.3 | 1.8 | 0.4 | 0.4 |  |  |
| Other HCs (Tg C) | 43.5 | 20.2 | 12.9 | 13.2 |  | 6.8 |

Table 3. Indication of uncertainty estimate for ozone precursors.

| Main source | Subcategory | Activity | Emission factors | Global and regional emissions |
| --- | --- | --- | --- | --- |
|  |  | data | CO | NOx | NMVOC | CO | NOx | NMVOC |
| Fossil fuel use | Fossil fuel combustion | S | M | M | M | M | M | M |
|  | Fossil fuel production | S | - | - | M | - | - | M |
| Biofuel | Biofuel combustion | L | M | M | M | L | L | L |
| Industry/ | Iron & steel production | S | M | M | L | M | M | L |
| solvent use | Non-ferro production | S | M | M | L | M | M | L |
|  | Chemicals production | S | M | M | L | M | M | L |
|  | Cement production | S | - | - | - | - | M | - |
|  | Solvent use | M | - | - | M | - | - | M |
|  | Miscellaneous | V |  |  | V |  |  | V |
| Landuse/ | Agriculture | S | - | - | - | - | - | - |
| waste | Biomass burning | L | M | L | L | L | L | L |
| treatment | Agricultural waste burning | L | L | L | L | L | L | L |
|  | Uncontrolled waste burning | L | - | - | L | - | - | V |
| Natural | Natural soils | M | - | L | - | - | L | - |
| sources | Natural vegetation | M | M | - | L | M | - | L |
|  | Oceans/wetlands | M | L | - | - | L | - | - |
|  | Lightning | S | - | L | - | - | L | - |
|  |  |  | CO | NOx | NMVOC | CO | NOx | NMVOC |
| All sources |  | - | - | - | - | M | M | L |

Notes:  Expert judgement of uncertainty ranges, which were assigned with the following classification in terms of order of magnitude of the uncertainty in mind: S = small (10%); M = medium (50%); L = large (100%); V = very large (>100%).

"-" Indicates that the compound is not applicable for this source or that emissions are negligible.

2.3 Temporal variation

For test-run purposes with several models a set of temporal (seasonal and diurnal) factors has been constructed for other anthropogenic sources (Figure 3a). This set is primarily based on (sometimes selected) Western European data. Therefore the representativity for other European countries and even more so for other world regions is highly uncertain. This provisional dataset is primarily meant for sensitivity assessments in atmospheric chemistry and climate models, awaiting a more comprehensive compilation and assessment of the relative importance for models. An example of have NOx emissions may be affected by seasonal variation of emissions is provided in Figure 3b, where the profiles for fossil fuel combustion sources have been aggregated to regional variation in total combustion emissions. Apparently, in the Northern Hemisphere regional emissions may vary up to 15% from a uniform distribution.

Figure 3a. Temporal profiles for different sources developed for test purposes: season (top) and diurnal (bottom) variation in TNO-TROTREP/POET profiles.

Figure 3b. Seasonality of regional NOx emissions from fossil fuel combustion based on TNO-TROTREP/POET profiles.

2.4 Emission changes over the 1990-2000 period

2.4.1 Anthropogenic emissions

The emission dataset has been extended and formatted so that it can be used in a user-friendly manner by the POET models. Emissions for the 1990-2000 period have also been developed, using a linear extrapolation. This extrapolation has been performed for each type of emissions for each species. The changes in the emissions reflect the 1990-1995 and 1995-1997 changes, which are summarized in Table 4.

Table 4: Anthropogenic emission trends 1990-1995 and 1995-1997.

| Period | CH4 emissions | CO emissions | NOx emissions |
| --- | --- | --- | --- |
| 1990-1995 | Global: 0% Agriculture -0% Waste handling +6% Fossil fuel -4% | Global: -0% Biomass burning +3% Biofuel +7% Fossil fuel -8% | Global: +2% Fossil fuel -0% Biofuel +9% Biomass burning +4% |
| 1995-1997 | Global: +1% former USSR (fSU): -9% S Asia: +4% | Global: +1% fSU and E Europe: -10% OECD Europe: -7% USA: +15% | Global: +3% fSU: -7% S Asia +16% SE Asia: +9% |

| Period | NMVOC emissions |
| --- | --- |
| 1990-1995 | Global: +4% Biofuel +7% Biomass burning 10%; without TVF*: -5% Fossil fuel +3% |
| 1995-1997 | Global: +0% former USSR (fSU): -13% Middle East +6% SE Asia: +8% |

* TVF = Temperate Vegetation Fires.

The totals emitted for different types of emissions are given in Table 5 for each year during the 1990-1999 period for carbon monoxide (5.a) and nitrogen oxides (5.b). The emissions have been grouped into two emission categories, technological and biofuel emissions.

Table 5a. Global anthropogenic CO emissions in 1990-1999 (Unit = Tg CO/year)

| Source category | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Fuel - industrial | 4.136 | 4.140 | 4.144 | 4.147 | 4.151 | 4.155 | 4.032 | 3.909 | 3.885 | 3.908 |
| Fuel - power | 1.332 | 1.368 | 1.405 | 1.441 | 1.477 | 1.514 | 1.540 | 1.566 | 1.600 | 1.636 |
| Fuel – other transf | 0.269 | 0.260 | 0.251 | 0.242 | 0.233 | 0.224 | 0.230 | 0.237 | 0.233 | 0.230 |
| Fuel – residential etc | 52.53 | 49.53 | 46.53 | 43.53 | 40.53 | 37.53 | 35.28 | 33.02 | 30.56 | 28.62 |
| Road transport | 199.5 | 198.7 | 198.0 | 197.2 | 196.5 | 195.7 | 195.7 | 195.7 | 195.3 | 197.5 |
| Non-road transport | 20.29 | 19.44 | 18.58 | 17.73 | 16.87 | 16.02 | 14.75 | 13.48 | 12.58 | 12.42 |
| International ships | 0.091 | 0.093 | 0.095 | 0.098 | 0.100 | 0.102 | 0.012 | 0.102 | 0.104 | 0.106 |
| Oil production | 8.517 | 8.631 | 8.744 | 8.858 | 8.971 | 9.085 | 9.311 | 9.537 | 9.705 | 9.879 |
| Coal fires | 16.12 | 16.12 | 16.12 | 16.12 | 16.12 | 16.12 | 16.12 | 16.12 | 16.12 | 16.12 |
| Iron and steel proc. | 34.22 | 33.59 | 32.96 | 32.33 | 31.70 | 31.07 | 31.14 | 31.20 | 30.80 | 30.41 |
| Aluminium proc. | 0.072 | 0.073 | 0.075 | 0.076 | 0.078 | 0.079 | 0.080 | 0.081 | 0.082 | 0.084 |
| Pulp and paper proc. | 0.532 | 0.553 | 0.573 | 0.594 | 0.615 | 0.635 | 0.601 | 0.566 | 0.571 | 0.576 |
| Waste incineration | 3.630 | 3.670 | 3.710 | 3.750 | 3.790 | 3.830 | 3.818 | 3.806 | 3.831 | 3.856 |
| Sum technological | 341.2 | 336.2 | 331.2 | 326.1 | 321.1 | 316.1 | 312.7 | 309.3 | 305.4 | 305.3 |
| Biofuel industrial | 4.483 | 4.553 | 4.623 | 4.694 | 4.764 | 4.835 | 4.986 | 5.136 | 5.230 | 5.323 |
| Biofuel power | 0.239 | 0.248 | 0.258 | 0.267 | 0.277 | 0.287 | 0.287 | 0.288 | 0.295 | 0.302 |
| Biofuel other transf | 6.567 | 6.686 | 6.806 | 6.926 | 7.045 | 7.165 | 7.165 | 7.165 | 7.251 | 7.337 |
| Biofuel residential | 204.4 | 207.2 | 210.1 | 213.0 | 215.9 | 218.8 | 221.4 | 224.0 | 226.9 | 229.7 |
| Biofuel transport | 0.284 | 0.294 | 0.305 | 0.315 | 0.325 | 0.336 | 0.337 | 0.338 | 0.345 | 0.353 |
| Sum biofuel | 215.9 | 219.0 | 222.1 | 225.2 | 228.3 | 231.4 | 234.2 | 237.0 | 240.0 | 243.0 |

Table 5.b. Global anthropogenic NOx emissions in 1990-1999  (Unit: Tg N/year).

| Source category | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Fuel - industrial | 3.328 | 3.333 | 3.338 | 3.343 | 3.348 | 3.353 | 3.301 | 3.249 | 3.252 | 3.256 |
| Fuel - power | 7.127 | 7.121 | 7.115 | 7.109 | 7.103 | 7.097 | 7.219 | 7.341 | 7.372 | 7.414 |
| Fuel – other transf | 0.835 | 0.798 | 0.761 | 0.725 | 0.688 | 0.651 | 0.661 | 0.670 | 0.675 | 0.681 |
| Fuel – residential etc | 1.019 | 1.010 | 1.000 | 0.990 | 0.980 | 0.970 | 0.946 | 0.921 | 0.908 | 0.897 |
| Road transport | 8.413 | 8.403 | 8.393 | 8.383 | 8.373 | 8.363 | 8.636 | 8.909 | 8.982 | 9.063 |
| Non-road transport | 1.548 | 1.513 | 1.479 | 1.444 | 1.409 | 1.374 | 1.335 | 1.295 | 1.259 | 1.236 |
| International ships | 2.607 | 2.671 | 2.734 | 2.798 | 2.862 | 2.925 | 2.925 | 2.925 | 2.970 | 3.015 |
| Oil production | 0.063 | 0.075 | 0.087 | 0.098 | 0.110 | 0.122 | 0.125 | 0.128 | 0.138 | 0.147 |
| Coal fires | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 |
| Iron and steel proc. | 0.292 | 0.290 | 0.288 | 0.286 | 0.284 | 0.283 | 0.286 | 0.289 | 0.289 | 0.288 |
| Chemistry proc. | 0.230 | 0.228 | 0.225 | 0.223 | 0.221 | 0.218 | 0.215 | 0.211 | 0.208 | 0.207 |
| Pulp and paper proc. | 0.043 | 0.045 | 0.047 | 0.048 | 0.050 | 0.052 | 0.052 | 0.052 | 0.053 | 0.054 |
| Cement proc. | 1.043 | 1.096 | 1.150 | 1.203 | 1.257 | 1.310 | 1.359 | 1.408 | 1.460 | 1.516 |
| Waste incineration | 0.041 | 0.042 | 0.042 | 0.043 | 0.043 | 0.044 | 0.044 | 0.045 | 0.045 | 0.046 |
| Sum technological | 26.67 | 26.71 | 26.74 | 26.78 | 26.81 | 26.84 | 27.18 | 27.52 | 27.79 | 27.90 |
| Biofuel industrial | 0.142 | 0.145 | 0.147 | 0.150 | 0.153 | 0.156 | 0.161 | 0.166 | 0.169 | 0.172 |
| Biofuel power | 0.113 | 0.120 | 0.128 | 0.136 | 0.143 | 0.151 | 0.151 | 0.152 | 0.157 | 0.163 |
| Biofuel other transf | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 | 0.003 |
| Biofuel residential | 1.887 | 1.914 | 1.941 | 1.968 | 1.995 | 2.022 | 2.046 | 2.071 | 2.097 | 2.123 |
| Biofuel transport | 0.014 | 0.014 | 0.015 | 0.015 | 0.016 | 0.016 | 0.016 | 0.016 | 0.017 | 0.017 |
| Sum biofuel | 2.16 | 2.20 | 2.23 | 2.27 | 2.31 | 2.35 | 2.38 | 2.41 | 2.443 | 2.478 |

2.4.2 Biomass burning emissions over the 1997-2001 period

Satellite fire products, which give the location of fires at a high spatial resolution, have the potential to construct inter-annual time series of fire activity, but the quantification of biomass burning emissions using the satellite products remains challenging. We have built an inventory of emissions resulting from tropical forest and savanna fires using the fire counts from the Advanced Thermal Scanning Radiometer (ATSR) satellite. The redistribution of the emissions from the distribution of fire pixels was done in several steps. First, an annual integral of CO2 emissions for forest and savanna fires using the Hao and Liu (1994) climatological biomass burning emissions is computed. Then, the annual average of fire counts from ATSR using the full 1997-2001 record is computed for forest and savannas. A monthly average of CO2 emissions over each 1x1 degree grid point is calculated, using the monthly integrated fire counts over the grid point and the corresponding annual average. The CO2 emission for each month over the observation period as a result of forest and savanna fires is shown in Figure 4, together with a comparison of the value provided by EDGAR 3.

Figure 4: CO2 emissions from tropical forest (top) and savanna (bottom) fires base on ATSR fire counts and comparison with the EDGAR 3 dataset.

The emissions of each chemical species considered in the models is then computed using the emission ratios provided by Andreae and Merlet (2001), and listed in Table 6.

Table 6: Emission ratios to CO2 for different types of burning (expressed as molecule per molecule of CO2).

|  | Deforestation | Savanna burning | Agricultural waste | Non-tropical fires |
| --- | --- | --- | --- | --- |
|  | molec./molec(C) | molec./molec(C) | molec./molec(C) | molec./molec(C) |
| CH4 | 1.13E-2 | 3.82E-3 | 4.5E-3 | 7.8E-3 |
| CO | 0.099 | 0.0619 | 0.088 | 0.102 |
| NOx (as NO2) | 1.41E-3 | 3.47E-3 | 2.22E-3 | 2.66E-3 |
| C2H6 | 1.07E-3 | 2.84E-4 | 8.64E-4 | 5.32E-4 |
| C3H8 | 9.0E-5 | 5.45E-5 | 3.16E-4 | 1.15E-4 |
| C2H4 | 1.86E-3 | 7.54E-4 | 1.33E-3 | 1.07E-3 |
| C3H6 | 3.49E-4 | 1.66E-4 | 6.34E-4 | 3.74E-4 |
| CH2O | 8.89E-4 | 2.23E-4 | 8.39E-4 | 1.4E-3 |
| Acetone | 2.85E-4 | 2.03E-4 | 2.9E-4 | 2.52E-4 |
| Other HC(1) | 6.25E-3 | 3.75E-3 | 4.5E-3 | 8.75E-3 |
| NH3 | 2.04E-3 | 1.64E-3 | 2.04E-3 | 2.19E-3 |
| SO2 | 2.38E-4 | 1.46E-4 | 1.67E-4 | 4.16E-4 |

(1)IMAGES/MOZART species

a Obtained by assuming that TNMVOC = the sum of all NMVOCs listed in Table 1 of Andreae and Merlet (2001).

2.4.3 Summary

The EDGAR 3 emission dataset for precursors has been extended over time, specified for various hydrocarbons, combined with new biomass burning data and formatted so that it can be used in a user-friendly manner in chemistry-transport models. The changes over the 1990-2000 period of the global emissions for CO, nitrogen oxides and one hydrocarbon, ethane (C2H6), are shown in Figure 5.

Figure 5: Evolution of the total surface emissions for different categories for the 1990-2000 period for CO, NOx and C2H6.

3. Natural emissions

The geographical distribution and seasonal variation of the biogenic emissions are adapted from the GEIA inventories (for nitrogen oxides, isoprene and terpenes) and from Müller and Brasseur (1995) (for carbon monoxide).

A detailed vegetation canopy model has been developed at IASB for the calculation of isoprene and terpenes emissions. This multi-layer model calculates the transfer of visible and near infra-red radiation in the canopy as well as the temperature of the leaves. It has been used in order to evaluate the uncertainties in the emission estimates by comparisons of the model predictions with campaign flux measurements at a number of sites: a mixed forest in the North-eastern US, two savanna sites in Southern Africa, and a forest in Amazonia. The model/data biases are typically a factor of two, except at the Amazonian site, where the model overpredicts the isoprene flux measurements by a factor between 5 and 10. This work is highlighted in the poster displayed below, which was presented at the EU symposium in Torino in September 2001.

4. Future emissions for the period up to 2020.

Different scenarios have been evaluated, based on scenarios prepared for the IPCC Special Report on Emission Scenarios (SRES) (IPCC, 2000). These scenarios include four groups of scenarios, all quite different in their regional and global assumptions with respect to economic development, cooperation and environmental and technological changes. The scenarios result in a highly different development of future anthropogenic emissions in different regions (i.e., large emission increases in low latitude developing countries, decreases in emissions in northern industrialized areas). Natural emissions have been assumed to stay constant.

Figure 6 : Driving forces for the IPCC/SRES scenarios

Different scenarios can be envisaged from the SRES package. These four scenarios can be described as follows (see Figure 6 ):

- A1: very rapid economy growth, introduction of new technology, low population growth;

- A2: very heterogeneous, high population growth, fragmented and slower technological changes;

- B1: convergent world, changes towards sustainability, same low population growth as A1;

- B2: changes towards local sustainability, moderate population- growth, less rapid economical and technological changes than in A1 and B1.

The different assumptions on the main driving forces are summarized in Figure 7, whereas the different impacts of these scenarios on global total and regional anthropogenic emissions of ozone precursors are presented in Figures 8 to 10. As illustrated in Figure 7, apart from changes in growth rates of population and income, the main changes between the #1 and #2 scenarios that determine the trend in emissions are the introduction of new (control) technologies. As indicated by Figures 9 and 10 the use of clean technology is assumed to occur in all regions, but to different degrees in different scenarios.

Figure 7 : Main driving forces in the four marker scenarios: index of 2020 values

Figure 8: Global changes of anthropogenic emissions during the 1990-2020 period (in %) in the IPCC markers of the four SRES scenarios.

Figure 9: Anthropogenic CO emission changes (in %) between 1990 and 2020 for the four IPCC marker SRES scenarios and four world regions.

Figure 10: Anthropogenic NOx emission changes (in %) between 1990 and 2020 for the four IPCC SRES scenarios and four different world regions.

The long-term relative changes in emissions of CH4, CO, NOx and hydrocarbons is presented in Figure 11 for different areas of the world, as indicated in Table 7.

Table 7 : List of the regions used in the EDGAR inventory and in Figure 11

| Region number | Region name | Region number | Region name |
| --- | --- | --- | --- |
| 1 | Canada | 9 | Africa |
| 2 | USA | 10 | Middle East |
| 3 | OECD Europe | 11 | South Asia |
| 4 | Japan | 12 | East Asia |
| 5 | Oceania | 13 | South East Asia |
| 6 | Eastern Europe | 14 | Greenland |
| 7 | Former USSR | 15 | Antarctica |
| 8 | Latin America | 16 | Oceans |

Figure 11: Long term historical trend in regional anthropogenic ozone precursor emissions 1890-1990; index 1890 = 100 (for definition of regions see Table 1) (source: Van Aardenne et al., 2001).

The methodology for creating emission scenarios on grid is very similar to the compilation of the gridded 1997 datasets (see Section 2.1). Per EDGAR standard source category and for each of the 13 continental EDGAR world regions (see Table 7), the emission trends were calculated relative to the 1995 emissions of the scenarios for each five year; for intermediate years the trend has been interpolated. Next, these region-specific and source-specific indices for 1995-2020 were applied as multipliers to the gridded 1995 emissions per source category, resulting in gridded emission patterns that have been scaled per each of the 13 world regions.

For these gridded emission scenarios, RIVM’s IMAGE 2 implementation of the SRES scenarios have been used, since these contain more detailed sources and regions thereby producing a more consistent, higher-resolution scenario than would be possible when using only the four SRES regions and main SRES source categories. Moreover, a large part of the non-energy source emissions in the SRES report have been based on IMAGE model results. The IMAGE 2 model is an integrated model for assessing the effects of human activities on global change (IMAGE team, 2002).

An analysis made of the global and regional ozone precursor trends in the four so-called marker scenarios, led to the selection of the A2 and B1 scenarios as priority scenarios for gridding to and including 2020. This was done as they differ most from the present emission levels (A2) or provide the most contrasting trends between compounds (B1). In addition to the regional scenarios, we had to make projections for international transport since these were not explicitly considered in the SRES scenarios. The development of regional fuel consumption for international air and water transport was based on the average elasticity to GDP observed for OECD and non-OECD regions in the period 1970-2000. Table 8 shows the calculated global total trends. Assuming no substantial changes in the emission factors, these indices were then used to scale the 1995 gridded emissions with a globally uniform factor. Natural emissions have been assumed to stay constant in the next 25 year time period. In Table 9 the changes over time of CO and NOx emissions from the most important sources are summarized for these two scenarios, whereas Table 10 illustrates the trend of total NMVOC emissions in the scenarios.

Table 8: Trends in international shipping and aviation in the A2 and B1 scenarios (1995 = 100)

| Source | Scenario | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| International shipping | A2 | 100 | 105 | 110 | 114 | 120 | 126 |
|  | B1 | 100 | 104 | 109 | 114 | 118 | 123 |
| Aviation | A2 | 100 | 112 | 126 | 138 | 153 | 168 |
|  | B1 | 100 | 112 | 124 | 136 | 148 | 161 |

The trends presented in the POET emission scenarios differ somewhat from the IPCC marker scenarios presented in Figures 8 to 10. This is due to differences between (regional) 1995 source strengths in the SRES scenarios and EDGAR 3.2 estimates for 1995 and the IMAGE 2.2 implementation of the SRES scenario. The POET scenario for for large scale biomass burning includes the use of updated emission factors from Andreae and Merlet (2001).  As shown in Figure 8, global emissions of CO, NOx and NMVOC in 2020 are in the B2 scenario some 30%-points lower than in the A2 scenario. For CO this results in an absolute decrease compared to 1990 for all world regions except Asia (Figure 9). For NOx in the B1 scenario a decrease over time was calculated for OECD and EIT countries (Figure 10).

Table 9: POET A2 and B1 Emission scenarios 1995-2020 for CO and NOx based on EDGAR 3.2 emissions in 1995 and IMAGE 2 .2 emission projections (Unit: Tg CO and Tg NOx-N)

|  | Global total | OECD | EIT | ALM | ASIA |
| --- | --- | --- | --- | --- | --- |
|  | 2020 | 1995 | 2020 | 1995 | 2020 | 1995 | 2020 | 1995 | 2020 | 1995 |
|  | A2 | B1 |  | A2 | B1 |  | A2 | B1 |  | A2 | B1 |  | A2 | B1 |  |
| CO emissions: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Road transport | 291 | 178 | 212 | 116.8 | 60.0 | 119.0 | 10.9 | 7.3 | 12.4 | 102.3 | 64.7 | 48.9 | 61.2 | 45.7 | 31.8 |
| Other fossil fuel | 64 | 48 | 66 | 11.2 | 7.3 | 11.0 | 14.6 | 11.3 | 23.3 | 11.9 | 11.5 | 6.0 | 26.4 | 17.9 | 25.8 |
| Ind. proc.1) | 59 | 44 | 36 | 18.6 | 9.4 | 15.5 | 10.0 | 5.7 | 6.9 | 10.1 | 9.6 | 3.2 | 19.8 | 19.2 | 10.1 |
| Subtotal technol. | 414 | 270 | 314 | 146.6 | 76.8 | 145.5 | 35.5 | 24.4 | 42.7 | 124.3 | 85.8 | 58.1 | 107.4 | 82.9 | 67.7 |
| Biofuel | 282 | 240 | 231 | 9.2 | 8.8 | 8.3 | 4.7 | 4.5 | 7.0 | 100.8 | 90.0 | 68.6 | 167.2 | 137.2 | 147.2 |
| Agric. waste burn. | 37 | 28 | 25 | 6.0 | 5.0 | 4.2 | 4.8 | 3.5 | 4.9 | 18.1 | 13.4 | 11.1 | 8.0 | 6.3 | 4.8 |
| Forest burning | 364 | 174 | 149 | 45.4 | 45.4 | 45.4 | 1.9 | 1.9 | 1.9 | 263.1 | 80.2 | 69.2 | 53.9 | 46.3 | 32.8 |
| Savanna burning | 106 | 118 | 162 | 14.8 | 14.9 | 10.7 | 0.0 | 0.0 | 0.0 | 87.8 | 100.3 | 148.4 | 2.8 | 2.4 | 3.4 |
| Subtotal biomass | 789 | 560 | 568 | 75.4 | 74.1 | 68.6 | 11.4 | 9.9 | 13.9 | 469.9 | 283.8 | 297.2 | 231.9 | 192.3 | 188.2 |
| Total | 1203 | 830 | 882 | 222.1 | 150.9 | 214.1 | 46.9 | 34.2 | 56.5 | 594.3 | 369.6 | 355.4 | 339.3 | 275.2 | 255.9 |
| NOx emissions: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Road transport | 9.6 | 6.5 | 8.4 | 3.0 | 2.1 | 4.7 | 0.4 | 0.2 | 0.4 | 3.6 | 2.5 | 2.0 | 2.6 | 1.7 | 1.3 |
| Other fossil fuel | 25.6 | 18.2 | 17.1 | 23.7 | 15.4 | 20.7 | 7.3 | 5.4 | 7.0 | 18.4 | 14.7 | 10.0 | 21.1 | 15.4 | 13.0 |
| Ind. proc.1) | 2.6 | 2.4 | 1.9 | 0.7 | 0.6 | 0.6 | 0.2 | 0.2 | 0.2 | 0.6 | 0.5 | 0.3 | 1.1 | 1.0 | 0.8 |
| Subtotal technol. | 37.8 | 27.1 | 27.3 | 27.4 | 18.1 | 26.0 | 7.9 | 5.8 | 7.5 | 22.5 | 17.7 | 12.3 | 24.9 | 18.2 | 15.1 |
| Biofuel | 2.8 | 2.2 | 2.2 | 0.1 | 0.1 | 0.1 | 0.0 | 0.0 | 0.1 | 1.1 | 0.8 | 0.6 | 1.6 | 1.3 | 1.4 |
| Agric. waste burn. | 0.5 | 0.4 | 0.3 | 0.1 | 0.1 | 0.1 | 0.1 | 0.0 | 0.1 | 0.2 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 |
| Forest burning | 2.8 | 1.5 | 1.3 | 0.6 | 0.6 | 0.6 | 0.0 | 0.0 | 0.0 | 1.8 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 |
| Savanna burning | 3.0 | 3.3 | 4.6 | 0.4 | 0.4 | 0.3 | 0.0 | 0.0 | 0.0 | 2.5 | 2.8 | 4.2 | 0.1 | 0.1 | 0.1 |
| Subtotal biomass | 9.1 | 7.4 | 8.5 | 1.2 | 1.2 | 1.0 | 0.1 | 0.1 | 0.2 | 5.6 | 4.4 | 5.4 | 2.1 | 1.8 | 1.8 |
| Total | 46.9 | 34.5 | 35.8 | 28.6 | 19.3 | 27.1 | 8.0 | 5.9 | 7.7 | 28.1 | 22.1 | 17.7 | 27.0 | 19.9 | 16.9 |

1)  Including  waste incineration.

N. B. Using the emission factors for biomass burning  from Andreae and Merlet (2001).

The trends presented in the POET emission scenarios differ somewhat from the IPCC marker scenarios presented in Figures 8 to 10. This is due to differences between (regional) 1995 source strengths in the SRES scenarios and EDGAR 3.2 estimates for 1995 and the IMAGE 2.2 implementation of the SRES scenario. The POET scenario for for large scale biomass burning includes the use of updated emission factors from Andreae and Merlet (2001).  As shown in Figure 8, global emissions of CO, NOx and NMVOC in 2020 are in the B2 scenario some 30%-points lower than in the A2 scenario. For CO this results in an absolute decrease compared to 1990 for all world regions except Asia (Figure 9). For NOx in the B1 scenario a decrease over time was calculated for OECD and EIT countries (Figure 10).

Table 10: POET A2 and B1 Emission scenarios 1995-2020 for total NMVOC (Unit: Tg NMVOC)

|  | Global total | OECD | EIT | ALM | ASIA |
| --- | --- | --- | --- | --- | --- |
|  | 2020 | 1995 | 2020 | 1995 | 2020 | 1995 | 2020 | 1995 | 2020 | 1995 |
|  | A2 | B1 |  | A2 | B1 |  | A2 | B1 |  | A2 | B1 |  | A2 | B1 |  |
| Road transport | 50.1 | 31.0 | 36.1 | 18.5 | 9.3 | 19.8 | 1.5 | 1.0 | 1.7 | 15.8 | 10.0 | 7.6 | 14.3 | 10.7 | 7.1 |
| Other fossil fuel | 69.6 | 67.2 | 43.4 | 8.6 | 6.6 | 8.2 | 14.8 | 11.7 | 13.2 | 38.5 | 41.8 | 17.1 | 7.7 | 7.1 | 4.9 |
| Ind. proc.1) | 43.5 | 32.1 | 28.1 | 19.7 | 13.5 | 17.0 | 4.5 | 2.6 | 3.9 | 9.7 | 7.7 | 3.3 | 9.6 | 8.3 | 4.0 |
| Subtotal technol. | 163.1 | 130.4 | 107.7 | 46.8 | 29.4 | 44.9 | 20.8 | 15.3 | 18.8 | 64.0 | 59.5 | 28.0 | 31.5 | 26.1 | 16.0 |
| Biofuel | 37.0 | 29.0 | 27.9 | 1.1 | 1.1 | 1.0 | 0.6 | 0.5 | 0.8 | 15.7 | 11.3 | 8.6 | 19.6 | 16.1 | 17.5 |
| Agric. waste burn2) | 2.6 | 2.0 | 1.8 | 0.4 | 0.4 | 0.3 | 0.3 | 0.2 | 0.3 | 1.3 | 0.9 | 0.8 | 0.6 | 0.4 | 0.3 |
| Forest burning2) | 15.8 | 7.0 | 5.9 | 1.1 | 1.1 | 1.1 | 0.0 | 0.0 | 0.0 | 12.2 | 3.7 | 3.2 | 2.5 | 2.1 | 1.6 |
| Savanna burn.2) | 4.1 | 4.5 | 6.3 | 0.6 | 0.6 | 0.4 | 0.0 | 0.0 | 0.0 | 3.4 | 3.9 | 5.7 | 0.1 | 0.1 | 0.1 |
| Subtotal biomass | 59.5 | 42.5 | 41.8 | 3.2 | 3.0 | 2.8 | 1.0 | 0.8 | 1.2 | 32.6 | 19.8 | 18.3 | 22.7 | 18.7 | 19.5 |
| Total | 222.6 | 172.8 | 149.5 | 49.9 | 32.5 | 47.7 | 21.8 | 16.1 | 20.0 | 96.6 | 79.4 | 46.3 | 54.3 | 44.8 | 35.5 |

1)  Including  waste incineration.

2)  Using the emission factors for total NMVOC from Andreae and Merlet (2001).

The A2 scenarios describe a very heterogeneous world with a high population growth, a  Business-as-Usual economic growth in industrialized countries, but slow economic growth in less-industrialized countries. Economic development is primarily regionally oriented and per capita economic growth and technological change are more fragmented and slower than in other scenarios. With a focus on regional (cultural) identity, environment has low-priority and there is a low rate of energy efficiency innovations and slow diffusion of technology. Coal use rises in many regions. Thus, we see a rise in global emissions of CO of over 30% of CO and NOx emissions and about 50% of total NMVOC emissions. This increase is mainly stemming from developing countries, where emissions from road transport are doubling in 2020 compared to 1995. For NOx and NMVOCs, also stationary emissions from fossil fuel combustion increase substantially in developing countries (60% or more) as well as emissions from tropical forest fires. Forest burning increases by almost 300% in Africa due to the high demand for agricultural land, having a major impact on regional and global CO emissions. In contrast savanna burning emissions decrease by about half. In OECD regions road transport emissions remain almost constant over time, except for NOx emissions which decrease by 1/3. However, precursors emissions in OECD regions still rise slightly by about 5% due to increasing trends in stationary combustion or solvent use. Figures 12 and 13 show the interannual trend in the emissions of major sources of CO and NOx from 1995 to 2020 for the A2 scenario.

Figure 12 : Change in the CO anthropogenic surface emissions for the 1995-2020 period for the A2 scenario.

Figure 13 : Change in the NOx anthropogenic surface emissions for the 1995-2020 period for the A2 scenario.

The B1 scenario assumes continuing globalization and economic growth, and a focus on the environmental and social - immaterial - aspects of life. This in combination with regulations and financial incentives leads to a rapid decline in energy-intensive and material-intensive economic activities as people become more open to the need for and relevance of more sustainable forms of development. Governments can effectively solve environmental problems using regulation, ecotaxing and burden-sharing as the main policy instruments. There is a rapid diffusion of resource-efficient technology (IPCC, 2000; IMAGE team, 2002). Thus, in the B1 scenario we see a decreases of global CO and NOx emissions of about 5% and an increase of about 15% of total NMVOC emissions. For road transport this shows by CO emissions in industrial countries decreasing about 50% and by an increase of about 1/3 in Asian regions in spite of high growth of road traffic. CO emissions  from biofuel combustion remain about the same, except in China where emissions are assumed to decrease by about 20%. In China also coal combustion emissions from the residential sector decrease about 40%. However, forest fire emissions  in Southeast Asia increase by 50%, while in Africa they increase more than 200% which are compensated by a decrease of 50% in CO emissions from savanna burning. The degree of deforestation and savanna burning depends on the pressure on the agricultural system to produce sufficient food at regional and global levels, respectively. For NOx similar observations as for CO can be made. However, for NMVOC stationary combustion emissions and emissions from solvents etc. are increasing substantially in developing countries.

When reviewing the trends of the two scenarios selected, the key features are often not found in a substantial increase of global emissions – except for NMVOC – but rather in the much different regional changes over time. The largest increases occur in developing regions. The overall trends in industrialized regions are rather similar except for CO in the A2 scenario, where a significant decrease of emissions from heating of buildings is projected for the EIT regions.

5. References

Andreae, M. O. and P. Merlet (2001) Emission of trace gases and aerosols from biomass burning, Global Biogeochemical Cycles, 15, 955-966.

Hao, W.M., and M.H. Liu, (1994) Spatial and temporal distribution of tropical biomass burning, Global Biogeochemical Cycles, 8, 495-503.

IMAGE team (2002) The IMAGE 2.2 implementation of the SRES scenarios; A comprehensive analysis of emissions, climate change and impacts in the 21st century. Eickhout B. (ed.). CD-rom publication/RIVM Report 481508018. RIVM, Bilthoven.

IPCC (2000) Special Report on Emissions Scenarios. Cambridge University Press, Cambridge. ISBN 0 521 80081 1.

Müller, J-F., and G. Brasseur (1995) IMAGES: a three-dimensional chemical transport model of the global troposphere, J. Geophys. Res., 100, 16445-16490.

Olivier, J.G.J. and J.J.M. Berdowski (2001) Global emissions sources and sinks. In: Berdowski, J., Guicherit, R. and B.J. Heij (eds.) "The Climate System", pp. 33-78. A.A. Balkema Publishers/Swets & Zeitlinger Publishers, Lisse, The Netherlands. ISBN 90 5809 255 0.

Olivier, J.G.J., J.J.M. Berdowski, J.A.H.W. Peters, J. Bakker, A.J.H. Visschedijk and J.P.J. Bloos (2001) Applications of EDGAR. Including a description of EDGAR V3.0: reference database with trend data for 1970-1995. RIVM, Bilthoven, report no. 773301 001 / NRP report 410200 051. ISBN 90-5851-077-8.

Olivier, J.G.J. (2002) Part III: Greenhouse gas emissions: 1. Shares and trends in greenhouse gas emissions; 2. Sources and Methods; Greenhouse gas emissions for 1990 and 1995. In: "CO2 emissions from fuel combustion 1971-2000", 2002 Edition, pp. III.1-III.31. International Energy Agency (IEA), Paris. ISBN 92-64-09794-5.

Peters, J.A.H.W. and J.G.J. Olivier (2003) EDGAR3/POET Emissions: 1997 Emissions and Scenarios for 1995-2020; Technical Background Information on Global and Regional Sectoral Emissions. RIVM, Bilthoven, report no. 773301003.

Van Aardenne, J.A., Dentener, F.J., Olivier, J.G.J., Klein Goldewijk, C.G.M. and J. Lelieveld (2001) A 1( x 1( resolution dataset of historical anthropogenic trace gas emissions for the period 1890-1990. Global Biogeochemical Cycles,15(4), 909-928.

Abstracts presented at international meetings

Development and Evaluation of a Canopy Environment Model for Regional and Global Predictions of Biogenic VOC Emissions, by S. Wallens, J.F. Müller and A. Guenther, International workshop on “Emissions of Chemical Species and Aerosols into the atmosphere”, June 2001, Paris, France.

Biogenic VOC emissions are very sensitive to leaf temperature and light intensity.  Thus an accurate description of canopy microclimate is a necessary component of a biogenic VOC emission model.  Predicting emissions at regional and global scales is challenging because of the need to specify general canopy characteristics for relatively broad vegetation types.  We present an improved canopy model that computes leaf temperature and light intensity for multiple vertical layers in a vegetation canopy.  Leaf temperature is calculated by energy balance and a detailed radiation transfer model is employed. The model is parameterized for seven basic growth forms.

We present fluxes estimates of isoprene, sensible heat, and latent heat for the seven basic growth forms and compare these measurements with relevant above canopy measurements from previous field studies.  In addition, we present a model sensitivity analysis and discuss priorities for future model refinement.

## Global emissions of ozone precursors: sources, trends and uncertainties, by Jos G.J. Olivier, presented at the Workshop ‘Air Pollution as a Climate Forcing’, Honolulu, USA, 29 April-3 May 2002

Global anthropogenic sources of ozone precursors CO, NOx, NMVOC and CH4 have been estimated for the period 1990-1997 based on national activity data (e.g. kg fuelwood combustion per year), emission factors (emissions per unit of human activity, e.g. kg CO/kg fuelwood combusted), and grid maps for spatial allocation of the emissions within a country (e.g. human population density). The results of a comprehensive study to estimate global emissions and their trend will be discussed briefly. Globally the largest anthropogenic sources of CO are residential biofuel use and road transport (both 25%), savannah burning (20%) and tropical forest fires (10%). For NOx the largest sources are road transport (25%), electric power generation (20%), industrial fossil fuel combustion and international shipping (both 10%), savannah burning (almost 10%), and residential biofuel use and cement production processes (both about 5%). For total non-methane volatile organic carbon emissions (NMVOC) largest emissions were found to be road transport (about 20%), oil production/handling, residential biofuel use and solvent use (each about 15%), whereas savannah burning and temperate vegetation fires contribute another 5% each. However, for modelling of the atmospheric chemistry its the most reactive compounds within total NMVOC that are important. Many of the key ones are being emitted by the largest sources, but not all. However, these sources are not distributed equally over  world regions, let alone individual countries. In OECD and Economies-In-Transition (former SU etc.) fossil-fuel use and industrial processes tend to dominate, while in other regions biomass burning, both large-scale as well as biofuel use, often is the largest source. Moreover, some of the largest sources tend to be concentrated in urban areas, e.g. road transport, fuel combustion by industry and power generation, others are most found in the rural area, as can be illustrated when looking at the emissions on a 1x1 degree grid. The shares of regions and sources in the global total and those that determine the trend in the 1990s will be discussed. In addition the uncertainty of the emission estimates will be discussed. The largest uncertainties are estimated for large-scale biomass burning, which may also vary substantially between years, biofuel use and for natural sources. Moreover, larger uncertainties appear in case of economies or technologies in transition (e.g. EIT, catalytic converter in cars); changes in emissions can be large in those regions, even in a few years. In these cases accurate monitoring of recent trends proves to be difficult. Subsequently, the recent regional emission trends 1990-1997 will be compared to the longer historical trend 1890-1990 as well as with four scenarios for future emissions for the period 1990-2020 developed by the IPCC. Historical trends of precursor emissions are quite different per region. It is concluded that future development of precursor emissions may show quite different characteristics in terms of size and sign of the growth but also the development could be quite different per compound.

Publications during the full duration of the project

Peer Reviewed Articles:

| Authors | Date | Title | Journal | Reference |
| --- | --- | --- | --- | --- |
| Van Aardenne, J.A., F. Dentener, J.G.J. Olivier, C.G.M. Klein Goldewijk, and J. Lelieveld | 2001 | A 1ox1o resolution dataset of historical anthropogenic trace gas emissions for the period 1890-1990 | Global Biogeo-chemical Cycles | 15, 909-928 |
| Wotawa, Gerhard, P. Novelli, M. Trainer and C. Granier, | 2001 | Inter-annual variability of summertime CO concentrations in the Northern Hemisphere explained by boreal forest fires in North America and Russia | Geophys. Res. Lett. | 28, 4575 |
| Endresen O., J. K. Sundet, E. Soergaard, S. Dalsoeren, G. Gravir, T. F. Berglen and I. S. A. Isaksen | 2003 | Emission from international sea transportation and environmental impact | J. Geophys. Res | 108, D17, 4560, doi:10.1029/2002JD002898 |

Non refereed literature:

| Authors / Editors | Date | Title | Event | Reference |
| --- | --- | --- | --- | --- |
| Olivier, J. | 2000 | Emission inventories of natural sources | IGAC Newsletter | 22, 5-9 |
| Olivier, J.G.J., and J.J.M. Berdowski | 2001 | Global emissions and sinks | in “The Climate System”, Eds. Berdowski, Guicherit and Heij , ISBN 90 5809 255 0 | pp 73-78, Balkema Publishers /Swets & Zeitlinger, NL |
| Olivier, J.G.J | 2001 | Shares and trends in greenhouse gas emissions | in “CO2 emissions from fuel combustion 1971-1999”, ISBN 92-64-08745-1 | pp III.3-III.7, International Energy Agency (IEA), Paris, |
| Olivier, J.G.J. | 2001/ 2002/ 2003 | CO2, CH4 and N2O emissions for 1990 and 1995: sources and methods | in “CO2 emissions from fuel combustion 1971-1999/ 2000/2001” | pp III.9-III.29, International Energy Agency (IEA), Paris, ISBN 92-64-08745-1. See below for 2002 and 2003 editions. |
| Olivier, J.G.J. | 2002/ 2003 | Part III: Greenhouse gas emissions: 1. Shares and trends in greenhouse gas emissions; 2. Sources and Methods; Greenhouse gas emissions for 1990 and 1995. | In: "CO2 emissions from fuel combustion 1971-2000/2001 | 2002 Edition, pp. III.1-III.31. International Energy Agency (IEA), Paris. ISBN 92-64-09794-5. 2003 Edition, 600 pages, ISBN 92-64-10225-6 |
| Olivier, J.G.J. | 2002 | On the Quality of Global Emission Inventories. Approaches, Methodologies, Input Data and Uncertainties. | Thesis Utrecht University. | Utrecht University. ISBN 90-393-3103-0. |
| Olivier, J.G.J. and K. Rypdal | 2002 | Inventories, Uncertainties and Verification, Conference report summary. | In: Van Ham, J., A.P.M. Baede, R. Guicherit and J.F.G.M. Williams-Jacobse (eds.):‘Non-CO2 greenhouse gases: scientific understanding, control options and policy aspects. | Proceedings, 3rd International Symposium, Maastricht, NL, 21-23 January 2002’, Millpress Science Publ. Rotterdam. ISBN 90-77017-70-4. |
| Olivier, J.G.J., J.A.H.W. Peters, J. Bakker, J.J.M. Berdowski, A.J.H. Visschedijk and J.P.J. Bloos:‘ | 2002 | EDGAR 3.2: Reference database with trend data of global greenhouse gas emissions for 1970-1995. | In: Van Ham, J., A.P.M. Baede, R. Guicherit and J.F.G.M. Williams-Jacobse (eds.), Non-CO2 greenhouse gases: scientific understanding, control options and policy aspects. | Proceedings, 3rd International Symposium, Maastricht, NL, 21-23 January 2002’, Millpress Science Publ. Rotterdam. ISBN 90-77017-70-4. |
| Van Amstel, A., J. Olivier and P. Ruyssenaars | 2002 | How to improve the monitoring of greenhouse gas emissions? | In: Van Ham, J., A.P.M. Baede, R. Guicherit and J.F.G.M. Williams-Jacobse (eds.):‘Non-CO2 greenhouse gases: scientific understanding, control options and policy aspects. | Proceedings, 3rd International Symposium, Maastricht, NL, 21-23 January 2002’, Millpress Science Publ. Rotterdam. ISBN 90-77017-70-4. |
| Olivier, J.G.J. | 2002 | Global emissions of ozone precursors: sources, trends and uncertainties. | In: J.E. Hansen (ed.) Proceeding of ‘Air Pollution as a Climate Forcing: A Workshop’. | Honolulu, Hawaii, April 29-May 3, 2002, pp. 57-58. NASA-GISS, New York, USA |
| Olivier, J.G.J., W. Winiwarter and C.-P. Chang | 2003 | Checks and verification at national and international level of national greenhouse gas inventories | IPCC Expert Meeting IPCC National Greenhouse Gas Inventories Programme Technical Support Unit (IPCC-NGGIP).. | Institute for Global Environmental Strategies (IGES), Hayama, Kanagawa, Japan. |
| Benkovitz, C.M., Akimoto, H., Corbett, J.J., Mobley, J.D., Olivier, J.G.J., Van Aardenne, J.A. and A.V. Vestreng | 2003 | Compilation of Regional to Global Inventories of Anthropogenic Emissions. | In: C. Granier, P. Artaxo and C.E. Reeves (eds.), Emissions of Atmospheric Trace Compounds, pp. 19-78. | Kluwer. In press. |

Presentations/Communications at international meetings:

| Authors / Editors | Date | Title | Event |
| --- | --- | --- | --- |
| Isaksen, I.S.A., J.K. Sundet, S.B. Dalrosen, | 2000 | The contribution of biomass burning to the global ozone budget and oxidation of chemical compounds in the troposphere | Quadrennial Ozone Symposium, Sapporo, Japan |
| S. Dalrosen, I.S.A. Isaksen, J.K. Sundet and G. Myhre | Sept. 2001 | The contribution of biomass burning to the global ozone budget and oxidation of chemical compo | EU Symposium: A changing atmosphere, Torino, Italy |
| Wallens, S., J.-F. Muller, and A. Guenther | Sept. 2001 | Development of a canopy environment model for new biogenic VOCs emissions inventories | EU Symposium: A changing atmosphere, Torino, Italy |
| Olivier, J.G.J. | April 2002 | Global emissions of ozone precursors: sources, trends and uncertainties. | Air Pollution as a Climate Forcing: A Workshop, Hawaii, USA |
| C. Granier et al., | Sept. 2002 | The POET European project | 7th IGAC Conference, Hersonissos, Greece |
| J. Hoelzemann, G. P. Brasseur, C. Granier, and M.G. Schultz | Sept 2002 | Quantifying global biomass burning emissions for chemistry transport modeling: a new inventory for MOZART | 7th IGAC/CACGP Conference, Hersonissos, Greece |
| Olivier, J.G.J. | Oct 2002 | Input data and uncertainties in emission inventories: Who cares? - Why and how should it be addressed? | CLRTAP International Workshop on Validation and Evaluation of Air Emission Inventories, Gothenburg, Sweden |
| S. B. Dalsoeren | Oct. 2002 | Emission from international sea transportation and environmental impact | 4th workshop on East Asia Atmospheric Environment, Taipei, Taiwan |
| Olivier, J.G.J. | Nov 2002 | Global emissions in EDGAR/HYDE; improvements on biomass burning emissions | Notes of a RIVM-JRC meeting on EDGAR-GBA, JRC, Ispra, Italy |
| Olivier, J.G.J. and J.A.H.W. Peters | Dec 2002 | Anthropogenic emissions: a) Global emissions 1970-1995; b) Uncertainties in global emissions. | Workshop on Anthropogenic and natural emission models, Mainz, Germany |
| J.J. Hoelzemann, G. P. Brasseur, T. Diehl, C. Granier, M.G. Schultz | April 2003 | The Global Wildfire Emission Model GWEM: Results and a Case Study with the atmospheric global: Chemistry Transport Model MOZART –2.4 | EGS-AGU-EGU Assembly, Nice, France |